## Slide 1: Introduction to E-BOX AETS
Vojtěch Míček
19.3.2026
Diploma thesis: E-BOX AETS

## Slide 2: Basic description of the system
Diploma thesis: E-box aets
Laboratory equipment for electrical testing of automotive components
Combines relay and MOSFET branches, local UI and PC control
Designed for faster, repeatable, safer and easier testing
AETS Automated Electrical Testing System

## Slide 3: Why was the device developed?
Diploma thesis: E-box aets
Acceleration of repetitive electrical tests
Universal platform across EE Teams
Reproducibility of test sequences.
Need in practice
Switching of tested branches
Fast switching capabilities
Basic internal supervision of test progress
Communication with host PC with option to remotely control the device
What it does
ON/OFF tests
Switching sequences
Fast switching for INRUSH current testing
Long-term cyclic tests
Typical usage

## Slide 4: Brief description of how the system works
Diploma thesis: E-box aets
PC/LabView Manual setup
MCU logic & sequence control
Relays MOSFETs
DUT
Measurement devices
Additional functions
Advanced UI, Trigger, Relay cycle counter & current monitoring, External MOSFET control
MOSFETs
Fast switching for precise timing, short pulses, and monitoring of transient signals.
Relays
Robust switching, low contact resistance, suitable for normal ON/OFF sequences and long-term cycles

## Slide 5: Brief description of how the system works
Diploma thesis: E-box aets

## Slide 6: Connectors and interfaces
Diploma thesis: E-box aets
Control Connectors
12 V DC power supply jack
2x BNC input for external control of MOSFETs
BNC TRIGGER output for synchronization
DSUB-9 CAN OUTPUT for extended communication
USB for connection to a PC and remote control
Test Connectors
  4 Relay Branches
  2 MOSFET switch pairs

## Slide 7: Complete Assembly
Diploma thesis: E-box aets

## Slide 8: System configuration
Diploma thesis: E-box aets
Select control mode
Configure channels and timing
Run test
Monitor test progress
Evaluate test results
System options
Trigger, communication and data storage in profiles.
MOSFETs
Channel enable, turn-on time, turn-off time, internal or external control selection, and number of cycles.
Relays
Channel enable, turn-on time, turn-off time, number of cycles, and internal current control limits.

## Slide 9: System configuration
Diploma thesis: E-box aets

## Slide 10: Basic navigation and modes
Diploma thesis: E-box aets
TEST
Run sequence with supervision. In case of failure, the system will switch to a safe state and report the error.
REMOTE
Control from a PC via USB. Suitable for automation and integration into laboratory workflow.
MANUAL
Local operation via display and encoder. Suitable for quick function checks, servicing, and simple sequences.
The display shows the basic status of the device, function selection, and test progress.
The encoder is used to navigate the menu, change parameters, and confirm selections.
The system can be controlled remotely using commands and telemetry/status information can be obtained.
Important operating data is stored in EEPROM and is retained in the event of a brownout.

## Slide 11: Basic navigation and modes
Diploma thesis: E-box aets
MANUAL
REMOTE
TEST

## Slide 12: Maximum values and performance
Diploma thesis: E-box aets
4 channels
Continuous current up to 2.5 A per branch
Maximum switching voltage: 60 VDC
RELAYS
2 pairs of back-to-back MOSFETs
Continuous current up to 5 A
Short-term(<300 µs) inrush up to 40 A
Max. switching voltage: 80 VDC
MOSFETS
Relay response time in the order of milliseconds
MOSFET rise/fall time << 100 µs
Switching dynamics

## Slide 13: How can the system make work easier for test engineers?
Diploma thesis: E-box aets
Faster repetition of test sequences without manual switching
Integration of multiple switching options into a single device
Ability to control the test locally or remotely from a PC depending on the type of task
Easier synchronization with an oscilloscope or generator via trigger/BNC inputs
Storage of operating data and basic diagnostics of error states
Suitable basis for further expansion of test scenario automation in the laboratory
AETS is a practical laboratory platform that combines:
robust switching
fast MOSFET actions
local and remote control
simple measurement synchronization
Goal: to simplify and speed up electrical component testing.
Conclusion

## Slide 14
THANK YOU